## Slide 1
Programming
Distributed Control Planes
Ryan Beckett (Princeton & MSR)
Ratul Mahajan (MSR)
Todd Millstein (UCLA)
Jitu Padhye (MSR)
David Walker (Princeton)
Propane

## Slide 2: Configuring Networks is Error-Prone
“Close to 3 in 4 of all new prefix advertisements were results of misconfiguration”
Causes:
  operator slips
  low-level details: filters, communities
  logical errors in plans
  misunderstanding of configuration semantics
  router bugs

## Slide 3: Configuring Networks is Error-Prone

## Slide 4: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic to go through AT&T over Verizon
  Enforce isolation between two locations
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Don’t leak internal services to the outside world
  Adhere to policies in the good times and the bad (failures)
Mechanisms: Device-by-Device
  Local decisions made independently on each device
  Several device-level actions together imply some higher-level behavior
  Failures interact with local decision-making algorithms in complex ways
GAP

## Slide 5: Recent Developments in Network Programming
A new suite of SDN programming languages provide:
  Simpler, centralized programming models
  Network-wide abstractions like paths
  Compositional construction of complex policies from simpler parts
  Examples include:
    Frenetic [ICFP ’11], PANE [HotSDN ’12], Fat Tire [HotSDN ’13], Pyretic [NSDI ’13], Merlin [CoNext ’13], FlowLog [NSDI ’14], NetKAT [POPL ’14], …
But they aren’t a panacea:
  They consider intra-domain routing but not inter-domain routing issues
  Programs don’t express preferences ahead of time in case of failures
  Their implementations don’t exploit existing network infrastructure
  One must still build controller infrastructure that is fault tolerant and scalable — issues often left undiscussed in academic projects

## Slide 6: Propane: Programming a Distributed Control Plane
A language for expression of high-level operator objectives with:
  regular paths and relative preferences with fall-backs in case of failures
  uniform abstractions for intra- and inter-domain routing
  network-wide constraints that make some low-level errors impossible to express
And a compiler that bridges the gap between high-level objectives and low-level distributed control plane mechanisms:
  efficient algorithms to synthesize a set of policy-compliant BGP configs
    reuse existing infrastructure
    fault tolerant and scalable
  failure analysis guarantees policy compliance under all failures

## Slide 7: This Talk
Two Examples (simplified but emblematic of the issues)
  Operator objectives and challenges
  Propane solutions
The Propane Compiler
  Intermediate representations
  Compilation steps
  Failure analyses
Wrap-up
  Future work
  Conclusions

## Slide 8: BGP Protocol
BGP Nodes:
  receive and filter announcements
    modifying attributes
  decide on the best route per prefix using announcement attributes:
    local preference, AS path length, …
  export and filter routes to neighbors
D
F
E
B
A
C
Prefix = 1.2.3.4/32

## Slide 9: BGP Protocol
BGP Nodes:
  receive and filter announcements
    modifying attributes
  decide on the best route per prefix using announcement attributes:
    local preference, AS path length, …
  export and filter routes to neighbors
D
F
E
B
A
C
Prefix = 1.2.3.4/32
{Path=C X, Comm={}, … }
{Path=B Y X, Comm={6054:10}, … }
{Path=A X, Comm={6054:10}, … }

## Slide 10: BGP Protocol
BGP Nodes:
  receive and filter announcements
    modifying attributes
  decide on the best route per prefix using announcement attributes:
    local preference, AS path length, …
  export and filter routes to neighbors
D
F
E
B
A
C
Prefix = 1.2.3.4/32
{Path=C X, Comm={}, … }
{Path=B Y X, Comm={6054:10}, … }
{Path=A X, Comm={6054:10}, … }

## Slide 11: BGP Protocol
BGP Nodes:
  receive and filter announcements
    modifying attributes
  decide on the best route per prefix using announcement attributes:
    local preference, AS path length, …
  export and filter routes to neighbors
D
F
E
B
A
C
Prefix = 1.2.3.4/32
{Path=C X, Comm={}, … }
{Path=B Y X, Comm={6054:10}, … }
{Path=A X, Comm={6054:10}, … }

## Slide 12: BGP Protocol
BGP Nodes:
  receive and filter announcements
    modifying attributes
  decide on the best route per prefix using announcement attributes:
    local preference, AS path length, …
  export and filter routes to neighbors
D
F
E
B
A
C
Prefix = 1.2.3.4/32

## Slide 13: Example I: A Backbone Network

## Slide 14: A Backbone Network
Peer
Prov
Cust
R1
R2
R4
R5
BGP Nodes:
  receive and filter announcements
    modifying attributes
  decide on the best route per prefix using announcement attributes:
    local preference, AS path length, …
  export and filter routes to neighbors
Notes: BGP is an inter-domain routing protocol…

## Slide 15: A Backbone Network
Goals:
  P1: Prefer to exit thru Cust > Peer > Prov
  P2: Disallow traffic between Prov and Peer
  P3: For Cust, prefer exit thru R1 > R2
  P4: Cust must be on path for its prefixes
Peer
Prov
Cust
R1
R2
R4
R5

## Slide 16: A Backbone Network
Goals:
  P1: Prefer to exit thru Cust > Peer > Prov
  P2: Disallow traffic between Prov and Peer
  P3: For Cust, prefer exit thru R1 > R2
  P4: Cust must be on path for its prefixes
Implementation Techniques:
  Compute and set local preferences consistently at all Peer-facing, Cust-facing, Prov-facing interfaces
  For Cust, ensure R2 local pref is lower than R1
Peer
Prov
Cust
R1
R2
R4
R5

## Slide 17: A Backbone Network
Goals:
  P1: Prefer to exit thru Cust > Peer > Prov
  P2: Disallow traffic between Prov and Peer
  P3: For Cust, prefer exit thru R1 > R2
  P4: Cust must be on path for its prefixes
Implementation Techniques:
  Use communities to mark the location an announcement entered the network
Peer
Prov
Cust
R1
R2
R4
R5

## Slide 18: A Backbone Network
Peer
Prov
Cust
R1
R2
R4
R5
Goals:
  P1: Prefer to exit thru Cust > Peer > Prov
  P2: Disallow traffic between Prov and Peer
  P3: For Cust, prefer exit thru R1 > R2
  P4: Cust must be on path for its prefixes
Implementation Techniques:
  More filters to drop undesirable routes

## Slide 19: A Backbone Network
Goals:
  Network-wide
  High-level
Implementation Techniques:
  Local, device-by-device
    Several devices configured to satisfy one goal, requires coordination & consistency
  Varied
    Filters, MEDs, Local Pref, …
GAP
Peer
Prov
Cust
R1
R2
R4
R5
Notes: Consider the backbone network. It has three neighbors, a customer Cust, a peer Peer, and a provider Prov.

## Slide 20: Propane
A Propane policy associates sets of ranked paths with prefixes:
  Such paths define the desired flow of traffic
  Paths stretch from other networks, through our network, back out to neighbors
  Preferences between sets of paths express desired behavior when faults occur

## Slide 21: Propane
define Routing = {
true => exit(R1 >> R2 >> Peer >> Prov)
}
P1: Prefer to exit thru Cust > Peer > Prov
P2: Disallow traffic between Prov and Peer
P3: For Cust, prefer exit thru R1 > R2
P4: Cust must be on path for its prefixes
Peer
Prov
Cust
R1
R2
R4
R5

## Slide 22: Propane
Peer
Prov
Cust
R1
R2
R4
R5
define Routing = {
true => exit(R1 >> R2 >> Peer >> Prov)
}
define Ownership = {
PCust => later(Cust)
}
P1: Prefer to exit thru Cust > Peer > Prov
P2: Disallow traffic between Prov and Peer
P3: For Cust, prefer exit thru R1 > R2
P4: Cust must be on path for its prefixes

## Slide 23: Propane
define transit(X) = enter(X) & exit(X)
define NoTransit = {
true => !transit(Peer|Prov)
}
P1: Prefer to exit thru Cust > Peer > Prov
P2: Disallow traffic between Prov and Peer
P3: For Cust, prefer exit thru R1 > R2
P4: Cust must be on path for its prefixes
Peer
Prov
Cust
R1
R2
R4
R5

## Slide 24: Propane
define transit(X) = enter(X) & exit(X)
define NoTransit = {
true => !transit(Peer|Prov)
}
define Main = Routing & Ownership & NoTransit
P1: Prefer to exit thru Cust > Peer > Prov
P2: Disallow traffic between Prov and Peer
P3: For Cust, prefer exit thru R1 > R2
P4: Cust must be on path for its prefixes
Peer
Prov
Cust
R1
R2
R4
R5

## Slide 25: Example II: A Data Center Network

## Slide 26: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Goals:
  P1: Announce global services externally as the aggregate PG
  P2: Do not announce local services externally
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG

## Slide 27: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Goals:
  P1: Announce global services externally as the aggregate PG
  P2: Do not announce local services externally
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
Consider X-G, X-H Failure:
  PL* announcements travel H-Y-D-X
  PL* announcements are then leaked
  Without failure, X selects direct H-X path, which is shorter

## Slide 28: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Goals:
  P1: Announce global services externally as the aggregate PG
  P2: Do not announce local services externally
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
Consider X-G, X-H Failure:
  PL* announcements travel H-Y-D-X
  PL* announcements are then leaked

## Slide 29: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
  disallow “valley” paths

## Slide 30: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
  disallow “valley” paths
Consider D-A, X-C Failure:

## Slide 31: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
  disallow “valley” paths
Consider D-A, X-C Failure:
  X and Y will hear PG2

## Slide 32: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
  disallow “valley” paths
Consider D-A, X-C Failure:
  X and Y will hear PG2
  X and Y will announce aggregate PG
PG
PG

## Slide 33: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
  disallow “valley” paths
Consider D-A, X-C Failure:
  X and Y will hear PG2
  X and Y will announce aggregate PG
  But PG1 is inaccessible through X because there is no valley routing
  An aggregation-induced black hole is created [See Le et al, CoNext ’11]
PG
PG
PG1 Traffic

## Slide 34: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
Implementation Techniques for X, Y:
  do export announce’s from C, D outside
  do not export announce’s from G,H outside
    appeal: X, Y do not need to know which prefixes are local vs global
  aggregate to PG if announce is subset of PG
  disallow “valley” paths
Moral:
  Reasoning about the interactions between failures and the device-level configs is hard
  Not a good idea for humans to be doing that

## Slide 35: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
P1: Traffic for prefixes for each TOR router must reach the router
P2: Do not announce local services externally
P3: Aggregation must be performed on global prefixes to reduce churn

## Slide 36: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
define Ownership = {
PG1 => end(A)
PG2 => end(B)
PL1 => end(E)
PL2 => end(F)
}
P1: Traffic for prefixes for each TOR router must reach the router
P2: Do not announce local services externally
P3: Aggregation must be performed on global prefixes to reduce churn

## Slide 37: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
define Ownership = {
PG1 => end(A)
PG2 => end(B)
PL1 => end(E)
PL2 => end(F)
}
define Routing = {
PL1 | PL2 => always(in)
}
P1: Traffic for prefixes for each TOR router must reach the router
P2: Do not announce local services externally
P3: Aggregation must be performed on global prefixes to reduce churn

## Slide 38: A Data Center Network
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
define Ownership = {
PG1 => end(A)
PG2 => end(B)
PL1 => end(E)
PL2 => end(F)
}
define Routing = {
PL1 | PL2 => always(in)
}
define Main =
Ownership & Routing &
agg(PG, in -> out)
P1: Traffic for prefixes for each TOR router must reach the router
P2: Do not announce local services externally
P3: Aggregation must be performed on global prefixes to reduce churn
compiler
discovers
lower bound
on # failures
required to
induce a
black hole

## Slide 39: Propane Language Summary
Programmers express high-level objectives via:
  Sets of inter- and intra-domain paths
  … defined by high-level abstractions: enter, exit, always, end, …
  … as well as preferences between those paths for failures
Programmers may also use:
  a small number of control constraints (agg)
  … while counting on the compiler for failure analysis
  … and combine constraints together using natural logical combinators

## Slide 40: Compiling Propane

## Slide 41: Propane Compiler
Propane
Regular
IR
Product
Graph IR
Abstract
BGP
CISCO
Juniper
Front End Constraint Language
Regular Expression-based IR
Topology
Failure
Analyses
Vendor-independent BGP
Vendor-specific configurations

## Slide 42: Propane Regular IR
Expand constraints in to regular expressions. EG:
  exit(X) =
  (out*.in+.(X ∩ out).out*)
  (out*.in*.(X ∩ in).out+)∪
  any = out*.in+.out*
  end(X) = any ∩ (Σ*.X)
Propane
Regular
IR
A few other simple transformations:
  conjunction of constraints ==> intersection of regular expressions
  conjunction of policies ==> prefix-by-prefix intersection
  nested preferences lifted: (x >> y) . z ==> (x.z) >> (y.z)

## Slide 43: Compilation: An Idealized Example
  (W.A.C.D.out) >> (W.B.in+.out)
Y
Z
W
B
A
D
E
C
X

## Slide 44: Reversed Automata from Policies
  1. (W.A.C.D.out)
  2. (W.B.in+.out)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
Policies
Reversed automata
tracks BGP message flow
Y
Z
W
B
A
D
E
C
X

## Slide 45: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
General Idea:
PG represents locations
reachable in the topology
while following the policy
(S,a,b)
Each PG node contains:
  topology node (S)
  state of automaton 1 (a)
  state of automaton 2 (b)
  set of preferences achieved
{2}
Two PG nodes are connected
if topology nodes are connected
and the automata make the
specified transition

## Slide 46: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start

## Slide 47: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)

## Slide 48: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)

## Slide 49: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)

## Slide 50: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 51: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Notes: One of the useful properties about the Product Graph…

## Slide 52: Constructing the Product Graph (PG)
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 53: Product Graph Mimization
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
  {2}
  {1}

## Slide 54: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Idea:
  Filter import messages according to incoming PG edges.
  For each internal location,
  decide which announcements to prefer,
  forward messages along PG edges
  Use a community value to tag the state of the automata
  For each external location,
  do nothing

## Slide 55: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,2),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 56: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 57: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 58: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 59: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
choice

## Slide 60: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
choice

## Slide 61: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
Highest preference
obtainable here
choice

## Slide 62: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
But there
could be a
failure!
choice

## Slide 63: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
Sometimes there is
no best choice
choice

## Slide 64: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 65: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
Prefer D’s
announce

## Slide 66: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
If we remove this edge,
the policy becomes unimplementable.
If we choose D’s announcement and
forward to A, the A-W link may fail
If we choose E’s announcement and
forward to B, the B-W link may fail
(or the A-W link may not fail and
we will have a sub-optimal route)

## Slide 67: Implementation (5,500 lines of F#)
Benchmarks:
  data center policies (~1600 routers) and backbone policies (~200 routers, many peers/router) from a large cloud provider
  policy from English docs
  Ignoring prefix, customer group and ownership definitions:
    31 lines for data center
    43 lines for backbone
Scaling (8 core Windows machine):
  10s/pfx (mean) for largest data center
  45s/pfx (mean) for largest backbone
  3 minutes total for the backbone
  9 minutes total for the data center
Propane
Regular
IR
Product
Graph IR
Abstract
BGP
CISCO
Juniper
Topology

## Slide 68: Wrap-Up

## Slide 69: Ongoing & Future Work
Infrastructure
  building a simulator
  more analyses, modeling communities, benchmarks
Transition technology
  synthesizing high-level policies from low-level configurations
Looking for other gaps
  high-level property low-level distributed mechanism
  for example: load and congestion
  other protocols (OSPF, OpenFlow), route redistribution
Dynamics
  combining local and global control to react to new events

## Slide 70: Summary
Propane users express high-level objectives.
Objectives involve both intra- and inter-domain constraints.
Failure analysis guarantees strong safety properties.
Compiler bridges the gap between objectives and device-by-device control plane configurations.
Propane
Regular
IR
Product
Graph IR
Abstract
BGP
CISCO
Juniper
Topology

## Slide 71: Propane Team
Ryan
Beckett
CEO
Ratul
Mahajan
Jitu
Padhye
Networking
Programming Languages
Todd
Millstein
David
Walker

## Slide 73: Failure Analysis

## Slide 74: Compilation: The Issue
X
B
A
C
D
E
Y
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B

## Slide 75: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
    Issue:
    Violation of soundness — take a path not specified by the policy
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 76: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
    Issue:
    Violation of soundness — take a path not specified by the policy
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)
    Soundness is easy to handle by filtering bad paths (filter at B)

## Slide 77: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
    B - Filter routes through D
    Issue:
    Violation of completeness — path with preference 2 exists, yet none is taken
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 78: Compilation: The Issue
X
B
A
C
D
E
Y
  Challenge:
    C - Prefer D over E?
    Issue:
    Violation of completeness — path with preference 2 exists, yet none is taken
    Completeness is hard: C must make decision NOW but failures can happen upstream
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 79: Product Graph IR
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)

## Slide 80: Product Graph IR
Y
Z
W
B
A
D
E
C
X
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)

## Slide 81: Product Graph Minimization
Goal: Improve failure safety analysis precision by removing nodes/edges not on any simple path
Graph dominators as a cheap approximation
(D,2,2) dominates (A,4,2)
Repeatedly remove:
Any nodes start can’t reach
Any nodes that can’t reach end
Any node X where some X′ postdominates X
Any edge from X to Y where some X′ postdominates Y
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)

## Slide 82: Product Graph Minimization
Goal: Improve failure safety analysis precision by removing nodes/edges not on any simple path
Graph dominators as a cheap approximation
(D,2,2) dominates (A,4,2)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
Repeatedly remove:
Any nodes start can’t reach
Any nodes that can’t reach end
Any node X where some X′ postdominates X
Any edge from X to Y where some X′ postdominates Y

## Slide 83: Product Graph Minimization
Goal: Improve failure safety analysis precision by removing nodes/edges not on any simple path
Graph dominators as a cheap approximation
(D,2,2) dominates (A,4,2)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
Repeatedly remove:
Any nodes start can’t reach
Any nodes that can’t reach end
Any node X where some X′ postdominates X
Any edge from X to Y where some X′ postdominates Y

## Slide 84: Product Graph Minimization
Goal: Improve failure safety analysis precision by removing nodes/edges not on any simple path
Graph dominators as a cheap approximation
(D,2,2) dominates (A,4,2)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
Repeatedly remove:
Any nodes start can’t reach
Any nodes that can’t reach end
Any node X where some X′ postdominates X
Any edge from X to Y where some X′ postdominates Y

## Slide 85: Product Graph Minimization
Goal: Improve failure safety analysis precision by removing nodes/edges not on any simple path
Graph dominators as a cheap approximation
(D,2,2) dominates (A,4,2)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
Repeatedly remove:
Any nodes start can’t reach
Any nodes that can’t reach end
Any node X where some X′ postdominates X
Any edge from X to Y where some X′ postdominates Y

## Slide 86: Failure Safety
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Case I:
Decision point (C, -, 2) and (C,3,2)
Only prefer one state if we are always better off
Can each step from (C,-,2) be simulated by a step from (C,3,2)?
Y
Z
W
B
A
D
E
C
X
1
2

## Slide 87: Failure Safety
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Case 1I:
Unique topology node (D,2,2)
Same paths and preferences node (D,2,2) regardless of failures
Can prefer X and Y equally and let the shortest path decide

## Slide 88: Configuration Minimization
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export comm←(4,2), comm← noexport
MED←80, peer←W
Router B
match peer=C
export comm←(-,2), comm←noexport
MED←81, peer←W
Router C
match[lp=99] peer=E, comm=(-,2)
export comm←(-,2), peer←B
match peer=D, comm=(2,2)
export comm←(3,2), peer←A,B
Router D
match regex=(X + Y)
export comm←(2,2), peer←C
…

## Slide 89: Failure Safety
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Definition:
Restricted graph Gi — the product graph restricted to nodes that can reach an accepting state of i or better

## Slide 90: Failure Safety
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
High-level Idea:
Can prefer C1 to C2 when:
∀i, ∃j, j≤i ∧ protect(Gj, C1, Gi, C2)
Simulation Relation:
For each step C2 can take, C1 can take an equivalent next step
If no equivalent next step, see if an equivalent dominator exists

## Slide 91: Failure Safety: Example
F
A
B
A
B
C
D
D
E
E
H
C
D
F
G
G
C1
C2

## Slide 92: Failure Safety: Example
F
A
B
A
B
C
D
D
E
E
H
C
D
F
G
G
C1
C2

## Slide 93: Failure Safety: Example
F
A
B
A
B
C
D
D
E
E
H
C
D
F
G
G
C1
C2

## Slide 94: Failure Safety: Example
F
A
B
A
B
C
D
D
E
E
H
C
D
F
G
G
C1
C2

## Slide 95: Failure Safety: Example
F
A
B
A
B
C
D
D
E
E
H
C
D
F
G
G
C1
C2

## Slide 96: Aggregation Safety
Global
Services
Local
Services
PG1
PG2
X
Y
C
D
A
B
G
H
E
F
PL1
PL2
PG
PG
start
A
X
C
D
G
H
end
E
F
Y
B
PG
PG1