## Slide 1: BGP Configuration (issues)
Configuration is distributed
  E.g., Inconsistent filtering
Low-level mechanisms used to implement abstractions
  Modifying local preference/tagging communities to affect later decisions
Control + data planes out of sync
  Routes don’t correspond to paths or vice versa
Asynchrony in message arrival order
  E.g., Non-deterministic path selection
Information control
  Don’t leak more information than necessary

## Slide 2
Peer
Provider
Customers
route selection
Peer
path export
path export
path export
BGP Process
1. Filtering + Route selection
2. Route Export

## Slide 3
T0
T0
T0
T0
T1
T1
T0
T0
T0
T0
T0
T0
T0
T0
T1
T1
T1
T1
AZ
AZ
AZ
T2
T2
T2
Datacenter
Region
T3
Peer region
Core Network

## Slide 4: BGP Configuration (issues)
Configuration is distributed
  E.g., Inconsistent filtering
Low-level mechanisms used to implement abstractions
  Modifying local preference/tagging communities to affect later decisions
Control + data planes out of sync
  Routes don’t correspond to paths or vice versa
Asynchrony in message arrival order
  E.g., Non-deterministic path selection
Information control
  Don’t leak more information than necessary

## Slide 5: Example Properties (Single AS)
Preferences
  Various forms of filtering (prefer no path)
  Prefer free peers over paid provider
  Prefer customers over others
  Prefer certain outgoing links (cold-potato routing)
Information control (export policy)
  Don’t let peers know about other peers
  Hide internal changes (prefix aggregation)

## Slide 6: Example Properties (Multiples ASes)
Data plane properties
  Locality (no valleys, don’t go higher than necessary)
  At least / most k equal cost paths
  Basic (non)reachability
  Close fail, disjoint paths
  No transit between peers
  All routers in a tier treat traffic similarly
Information control (export policy)
  Don’t let peers know about other peers
  Hide internal changes (prefix aggregation)
  Traffic X does not leak beyond tier 1

## Slide 7: Abstractions (Primitives)
Route Selection
  Filtering
  Path preferences
Data plane reachability
  Paths
Information control
  Which paths to export
  Should specific prefixes be hidden (aggregated)

## Slide 8: Other Considerations
Traffic engineering
  Split traffic over all shortest paths
  Implement QoS
Efficiency
  Symmetrical policies and topologies
  Hierarchical structure maybe makes checking e.g., all pairs reachability easier
Soft vs Hard constraints
  E.g., locality can be violated if there is a failure