## Slide 1
Propane: Programming
Distributed Control Planes
Ryan Beckett (Princeton, MSR)
Ratul Mahajan (MSR)
Todd Millstein (UCLA)
Jitu Padhye (MSR)
David Walker (Princeton)

## Slide 2: Configuring Networks is Error-Prone
50-80% of outages are the result of human error
-Juniper 2008
~60% of network downtime is caused by human error
-Yankee group 2002

## Slide 3: Configuring Networks is Error-Prone
“Close to 3 in 4 of all new prefix advertisements were results of misconfiguration”
~1500 ASes affected by outages every day

## Slide 4: Configuring Networks is Error-Prone

## Slide 5: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic go through AT&T over Sprint
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Ensure traffic goes through X
  Adhere to policies even when failures occur
GAP

## Slide 6: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic go through AT&T over Sprint
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Ensure traffic goes through X
  Adhere to policies even when failures occur
GAP

## Slide 7: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic go through AT&T over Sprint
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Ensure traffic goes through X
  Adhere to policies even when failures occur
Mechanisms: Device-by-Device
  Local decisions made independently on each device
  Several device-level actions together imply some higher-level behavior
  Failures interact with local decision-making algorithms in complex ways
GAP

## Slide 8: Why use BGP?
Advantages
  Allows for local policy among nodes
  Massively scalable — hundreds of thousands of IP prefixes
  Fully distributed — does not require global knowledge of network state
BGP in the Wild
  Inter-domain routing between Autonomous Systems (AT&T, Sprint)
  Intra-domain routing in data centers
AT&T
Sprint
Notes: If so hard to configure, why is BGP used, and how is it used?

## Slide 9: What about SDN?
Software Defined Networks
  Simpler, centralized programming models
  Network-wide abstractions like paths
  Centralized controller programs the network
But they are not a panacea:
  Do not usually help with inter-domain routing
  Latency, and scalability can be problematic for large networks
  Require careful design and engineering to be robust to failures
  Their implementations don’t exploit existing network infrastructure

## Slide 10: Propane: Programming a Distributed Control Plane
I) Language for expressing high-level operator objectives with:
  Network-wide programming abstraction
  Uniform abstractions for intra- and inter-domain routing
  Paths constraints and relative preferences with fall-backs in case of failures
AS 1
AS 2
AS 3

## Slide 11: Propane: Programming a Distributed Control Plane
2) Compiler to generate a low-level distributed implementation:
  Efficient algorithms to synthesize a set of policy-compliant BGP configs
  Static analysis guarantees policy compliance under all failures
11￼
Backup
Network partition — drop

## Slide 12: Border Gateway Protocol (BGP)
  Routers send advertisements for a destination (e.g., 16.4.0.0/16)
  Advertisements contain the AS path traffic would take
  Each router applies local policy to choose best route
    Import filters drop advertisements or modify attributes
    Highest preference is chosen. Path length as a tie breaker
    Export filters drop advertisements or modify attributes
X
local-pref←100
local-pref←99
tag←“foo”
drop

## Slide 13: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 14: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
path = A
path = A
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 15: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 16: Border Gateway Protocol (BGP)
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
path = CA
X
X

## Slide 17: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 18: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
path = BCA
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A
X

## Slide 19: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 20: Border Gateway Protocol (BGP)
A
D
C
E
16.4.0.0/24
16.4.1.0/24
B
16.4.2.0/24
16.4.0.0/16
Aggregation (Route summarization)
  Advertise a more general subnetwork
  Information hiding for routers
  Reduces router table size and improves stability

## Slide 21: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers

## Slide 22: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Attempt (1)
  Don’t export from G, H to external
  Aggregate externally as PG
PG
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers

## Slide 23: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
PG
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Attempt (1)
  Don’t export from G, H to external
  Aggregate externally as PG

## Slide 24: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Attempt (1)
  Don’t export from G, H to external
  Aggregate externally as PG
  X,Y block routes through each other

## Slide 25: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
PG
PG
Attempt (1)
  Don’t export from G, H to external
  Aggregate externally as PG
  X,Y block routes through each other

## Slide 26: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Traffic
for PG1
dropped
Attempt (1)
  Don’t export from G, H to external
  Aggregate externally as PG
  X,Y block routes through each other

## Slide 27: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Traffic
for PG1
dropped
Aggregation-Induced Black Hole!
Attempt (1)
  Don’t export from G, H to external
  Aggregate externally as PG
  X,Y block routes through each other

## Slide 28: Example 1: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers

## Slide 29: Example 2: Backbone Network
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 30: Example 2: Backbone Network
tag(“Peer”)
16.4.0.0/16
block(“Peer”)
Goals
  Prevent transit between peers ($$$)
tag(“Peer”)
block(“Peer”)
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 31: Example 2: Backbone Network
tag(“Peer”)
16.4.0.0/16
block(“Peer”)
Goals
  Prevent transit between peers ($$$)
  Prefer R2 > R1 > Peer ($$$)
tag(“Peer”)
block(“Peer”)
lp←100
lp←99
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2
lp←101

## Slide 32: Example 2: Backbone Network
tag(“Peer”)
16.4.0.0/16
block(“Peer”)
Goals
  Prevent transit between peers ($$$)
  Prefer R2 > R1 > Peer ($$$)
  Filter customer by prefix (security)
tag(“Peer”)
block(“Peer”)
lp←99
filter(16.4.0.0/16, _Princeton)
lp←100
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2
lp←101
filter(16.4.0.0/16, _Princeton)

## Slide 33: Example 2: Backbone Network
define Peer = {Sprint, Level3}
define NoTransit = {
true => !transit(Peer,Peer)
}
  Prevent transit between peers
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 34: Example 2: Backbone Network
…
define Preferences = {
true => exit(R2 >> R1 >> Peer)
}
  Prefer R2 > R1 > Peer
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 35: Example 2: Backbone Network
…
define Ownership = {
16.4.0.0/16 => end(Princeton),
}
define Main =
Preferences & Ownership & NoTransit
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2
  Filter customer by prefix

## Slide 36: Propane: Summary
High-level language
  Single, network-wide policy
  Program using constraints and preferences
  Create new, reusable abstractions (e.g., transit traffic)
  Configure the network modularly
Compiler
  Automatically generates filters, preferences, community values, etc
  Static analysis guarantees policy compliance under all failures
  Lower bound on failures for aggregation-induced black holes

## Slide 37: Compilation
Propane
Regular
IR
Product
Graph IR
…
Quagga
Front End Constraint Language
Regular Expression-based IR
Failure
Analyses
Vendor-independent BGP
Vendor-specific configurations
Abstract
BGP
Topology

## Slide 38: Propane Regular IR
Propane
Regular
IR
define Ownership =
{PG1 => end(A)
PG2 => end(B)
PL1 => end(E)
PL2 => end(F)
true => exit(Peer1 >> Peer2)}
define NoTransit =
{true => !transit(Peer,Peer)}
define Locality =
{PL1 | PL2 => always(in)}
define Main =
Ownership & Locality & NoTransit
      & agg(PG, in -> out)
Step 1: Combine modular constraints

## Slide 39: Propane Regular IR
Propane
Regular
IR
PG1 => !transit(Peer,Peer) & end(A)
PG2 => !transit(Peer,Peer) & end(B)
PL1 => !transit(Peer,Peer) & always(in) & end(E)
PL2 => !transit(Peer,Peer) & always(in) & end(F)
true => !transit(Peer,Peer) & exit(Peer1 >> Peer2)
Prefix-by-prefix intersection of constraints

## Slide 40: Propane Regular IR
Step 2: Expand constraints in to regular expressions
  exit(X) =
  (out*.in+.(X ∩ out).out*)
  (out*.in*.(X ∩ in).out+)|
  any = out*.in+.out*
  end(X) = (Σ*.X)
Propane
Regular
IR
Step 3: Reduced syntax
  always(X) =
  (X)*
  true => A.(X >> Y).out*
  true => (A.X.out*) >> (A.Y.out*)
  start(X) =
  avoid(X) =
  waypoint(X) =
  (X.Σ*)
  (!X)*
  (Σ*.X.Σ*)

## Slide 41: Compilation: An Idealized Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:
  enter(A) & exit(D) >> enter(B) & exit(out)
  Policy:

## Slide 42: Compilation: An Idealized Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:
  enter(A) & exit(D) >> enter(B) & exit(out)
  Policy:

## Slide 43: Compilation: An Idealized Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:
  enter(A) & exit(D) >> enter(B) & exit(out)
  Policy:

## Slide 44: Reversed Automata from Policies
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
Policy:
Reversed automata
tracks BGP message flow
B
A
D
E
C
Z
Y
X
W
  1. (W.A.C.D.out)
  2. (W.B.in+.out)

## Slide 45: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 46: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 47: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 48: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 49: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)
(A,4,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 50: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)
(A,4,2)
(W,5, -)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  {1}

## Slide 51: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(Y,1,1)
(X,1,1)
(D,2,2)
(C,3,2)
(A,4,2)
(W,5, -)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  {1}

## Slide 52: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 53: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
Notes: One of the useful properties about the Product Graph…

## Slide 54: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 55: Constructing the Product Graph (PG)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
Compact representation of all paths through
the topology subject to policy constraints

## Slide 56: Constructing the Product Graph (PG)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  B
  ACDE

## Slide 57: PG Minimization (Loop analysis)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
  {2}
  {1}
Must end at W

## Slide 58: Compilation to BGP:
Idea 1: Restrict advertisements to PG edges
  Encode PG state in community tag
  Incoming edges — import filters
  Outgoing edges — export filters
Let BGP find some allowed path dynamically
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 59: Compilation to BGP:
C allows import from D with tag (2,2)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 60: Compilation to BGP:
C exports to A,B with tag (3,2)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 61: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
(-,2)
(2,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 62: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
(-,2)
(3,2)
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 63: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
(-,3)
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 64: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
(-,4)
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 65: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
Not ideal!
A better path exists in the
network, but is not used!

## Slide 66: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Idea 2: Find local preferences
Let BGP find the best allowed path dynamically
  Direct BGP towards best path
  Under all combinations of failures
  Frame in terms of graph algorithms

## Slide 67: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 68: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 69: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 70: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 71: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
choice

## Slide 72: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
choice

## Slide 73: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
Highest preference
obtainable here
choice

## Slide 74: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
But there
could be a
failure!
choice

## Slide 75: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
Sometimes there is
no best choice
choice

## Slide 76: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 77: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
Prefer D’s
announce

## Slide 78: Compilation to BGP:
B
A
D
E
C
Z
Y
X
W
The implementation always uses the best available path
B
A
D
E
C
Z
Y
X
W
drop from C
Implementation: C prefers D to E and tags accordingly
Backup path
Backup path
  enter(A) & exit(D) >> enter(B) & exit(out)
  Policy:

## Slide 79: Implementation
Benchmarks:
  Network configurations from Microsoft’s networks (Policy from English docs)
  Data center policies (~1400 routers)
  Backbone policies (~200 routers, many peers/router)
  Ignoring prefix, customer group and ownership definitions:
    31 lines for data center
    43 lines for backbone
Propane
Regular
IR
Product
Graph IR
Abstract
BGP
…
Quagga
Topology

## Slide 80: Compilation Time
Data center (< 9 min)
Backbone (< 3 min)
  Parallelize compilation by prefix
  Use artificial topology to explore scalability

## Slide 81: Configuration Size
Data center
Backbone
  Perform configuration minimization during generation
  Avoid using community tags when choices are unambiguous
  Fall-through elimination of route maps